## Slide 1
GRADUATION PROJECT DEFENSE
GridGuard Khartoum
PPO-assisted load shedding and energy management for developing countries
Murtada Asim Ibrahim Bakhit (18-317)
Suliman Elawad Suliman Babiker (18-310)
Abdalhay Abass Mobarak Abass (15-306)
Offline research simulation | August 2026
Notes: Open with the project question: can a learned policy allocate limited modeled supply more effectively than a traditional schedule?
[Sources]
- docs/source/graduation-project-proposal.pdf
- docs/REPORT.md
[/Sources]

## Slide 2
GRIDGUARD KHARTOUM
2
OFFLINE GPU RESEARCH SIMULATION
A shortage creates seven simultaneous allocation choices
Protect Hospital, Water, and Bakery demand
Use the available supply without exceeding it
Share service across seven modeled localities
Synthetic decision-support scope - not a live grid controller
Notes: Frame the problem as constrained allocation, not a claim that the simulator models the full electrical network. The schematic provides presentation context only.
[Sources]
- docs/METHODOLOGY.md (Simulation domain; Limitations)
- docs/assets/screenshots/overview.png
[/Sources]

## Slide 3
GRIDGUARD KHARTOUM
3
OFFLINE GPU RESEARCH SIMULATION
The proposal became a clean, auditable desktop system
Seeded scenarios
Shared CUDA tensors
PPO and Fixed Rotation
Paired evidence
Desktop replay
Controller evidence path
Demand projection
Display only - never enters PPO, dispatch, reward, or benchmark evidence
Offline after installation | hash-bound artifacts | fail-closed startup
Notes: Walk left to right. The controller path and display-only forecast are deliberately separated so a presentation feature cannot silently change the claim.
[Sources]
- docs/IMPLEMENTATION.md (System overview; Display-only forecast)
- docs/decisions/ADR-001-gpu-runtime.md
[/Sources]

## Slide 4
GRIDGUARD KHARTOUM
4
OFFLINE GPU RESEARCH SIMULATION
PPO and Fixed Rotation receive exactly the same scenario
96
independent base draws
x 3
288
matched scenario conditions
x 2
576
controller-scenario evaluations
PPO
32-value causal observation Learned 7-locality joint action
Fixed Rotation
Three-hour schedule blocks No demand or fairness observation
Every stored delta is PPO - Fixed Rotation
Notes: Stress the pairing: both controllers receive the same immutable Scenario object. The 288 conditions are severity variants of 96 independent base draws, not 288 independent draws; together they produce 576 controller-scenario evaluations.
[Sources]
- docs/METHODOLOGY.md (Controller decisions; Matched evaluation design)
- data/evidence/paired-benchmark.json, SHA-256 2c3e71e48c4c7bff4fe609d42a76ca4f770f6dd717cd7d45d5e8e0d99fdf2d11
[/Sources]

## Slide 5
GRIDGUARD KHARTOUM
5
OFFLINE GPU RESEARCH SIMULATION
GPU-first simulation, PPO inference, and paired bootstrap
PyTorch
scenarios simulation PPO inference
cuda:0
no CPU fallback
CuPy
cluster bootstrap CUDA sort linear percentiles
Validated presentation runtime
RTX 5060 Laptop GPU | PyTorch 2.8.0+cu128
CUDA 12.8 | CuPy 14.1.1 | DLPack coherence
Startup blocks on GPU, model, evidence, or provenance failure
Notes: The performance-critical scenario, simulation, PPO, metric, and bootstrap paths run on CUDA. One explicit final host transfer supports canonical evidence assembly and validation; it is not a controller fallback. The release gate validates Torch, CuPy, CUDA, DLPack sharing, the PPO artifact, and evidence before launch.
[Sources]
- docs/IMPLEMENTATION.md (GPU-first execution; Verification strategy)
- docs/decisions/ADR-001-gpu-runtime.md
[/Sources]

## Slide 6
GRIDGUARD KHARTOUM
6
OFFLINE GPU RESEARCH SIMULATION
The desktop replays one audited GPU scenario
Switch controller | scrub 24 hours | inspect locality | forecast is DISPLAY ONLY
Notes: Demo this after the slide: choose a shortage and seed, run once, then change controller and hour without changing the scenario. Point out demand, served MW, critical ratio, sector service, and the display-only next-hour projection.
[Sources]
- docs/IMPLEMENTATION.md (Desktop presentation)
- docs/assets/screenshots/live.png
[/Sources]

## Slide 7
GRIDGUARD KHARTOUM
7
OFFLINE GPU RESEARCH SIMULATION
PPO protects nearly all modeled critical demand
99.72%
PPO critical-service ratio
42.63%
Fixed Rotation
Critical service
42.63%
99.72%
+57.09 pp
Critical-outage locality-hours 102.07 -> 18.67
Notes: This is the strongest proposal-facing result. The critical-service ratio is modeled critical energy served divided by critical demand. Critical-outage locality-hours use the locked 99% threshold and are diagnostic, not a bootstrap endpoint.
[Sources]
- docs/RESULTS.md (Reproduced paired aggregate comparison)
- data/evidence/paired-benchmark.json
[/Sources]

## Slide 8
GRIDGUARD KHARTOUM
8
OFFLINE GPU RESEARCH SIMULATION
PPO serves 2,008 MWh more and uses supply more effectively
Served energy
4,552 MWh
6,560 MWh
Utilization
71.22%
97.65%
Curtailed energy
Fixed 6,142 MWh
PPO 4,134 MWh
+2,008 MWh served
+26.43 pp utilization
-2,008 MWh curtailed
Notes: Served and curtailed energy are complementary under the energy identity, so present them as two views of the same allocation change rather than independent endpoints.
[Sources]
- docs/RESULTS.md (Reproduced paired aggregate comparison)
- data/evidence/paired-benchmark.json
[/Sources]

## Slide 9
GRIDGUARD KHARTOUM
9
OFFLINE GPU RESEARCH SIMULATION
All seven paired intervals favor PPO
Outcome
PPO - Fixed
Cluster-bootstrap 95% interval
Episode reward
+9.54
[9.54, 9.55]
Critical service
+57.09 pp
[57.06, 57.11] pp
Utilization
+26.43 pp
[26.32, 26.53] pp
Jain fairness
+9.16 pp
[9.09, 9.23] pp
Served energy
+2,008 MWh
[2,000, 2,017] MWh
Curtailed energy
-2,008 MWh
[-2,017, -2,000] MWh
Switching rate
-3.11 pp
[-3.48, -2.75] pp
10,000 deterministic seed-stratified paired cluster replicates
Notes: Positive favors PPO for higher-is-better outcomes; negative favors PPO for lower-is-better outcomes. The bootstrap resamples 96 base-draw clusters inside seed strata and keeps all 3 shortage variants together.
[Sources]
- docs/METHODOLOGY.md (Paired uncertainty calculation)
- docs/RESULTS.md (Paired differences and 95% intervals)
- data/evidence/paired-benchmark.json, SHA-256 2c3e71e48c4c7bff4fe609d42a76ca4f770f6dd717cd7d45d5e8e0d99fdf2d11
[/Sources]

## Slide 10
GRIDGUARD KHARTOUM
10
OFFLINE GPU RESEARCH SIMULATION
The advantage is consistent, not driven by one seed
9 / 9
shortage-by-seed cells favor PPO for every primary outcome
Reward
9/9
Critical service
9/9
Utilization
9/9
Fairness
9/9
Served energy
9/9
Curtailed energy
9/9
Safety and diagnostics
0.00%
power-balance violation rate in both controllers
-3.11 pp
aggregate switching rate
Oversubscription stays diagnostic: direction was mixed across cells
Notes: All 6 primary outcomes favor PPO in all 9 cells. Switching favors PPO overall but in 7 of 9 cells. Oversubscription is lower in aggregate for PPO but mixed by cell, so it is not presented as a consistent primary advantage.
[Sources]
- docs/RESULTS.md (Consistency across the nine evaluation cells)
- data/evidence/paired-benchmark.json, SHA-256 2c3e71e48c4c7bff4fe609d42a76ca4f770f6dd717cd7d45d5e8e0d99fdf2d11
[/Sources]

## Slide 11
GRIDGUARD KHARTOUM
11
OFFLINE GPU RESEARCH SIMULATION
The evidence answers the proposal - within a strict boundary
What this establishes
PPO beats Fixed Rotation in the locked simulator
Critical-service protection and fairness improve
The result is reproducible from pinned artifacts
The desktop demonstrates one shared scenario honestly
What this does not establish
Field performance on Sudan's electrical grid
Network stability, voltage, or protection behavior
Superiority over every possible controller
Forecast accuracy from real operational data
Historical evidence stored 18 batch-cell summaries. Episode rows and intervals were regenerated from the audited simulator and frozen PPO checkpoint.
Notes: This boundary is part of the result, not a weakness to hide. The accepted historical artifact did not contain episode rows, so the paired rows and intervals are a reviewed regeneration, not reconstructed historical observations.
[Sources]
- docs/RESULTS.md (Two evidence layers; Limitations)
- docs/METHODOLOGY.md (Limitations and threats to validity)
[/Sources]

## Slide 12
GRIDGUARD KHARTOUM
12
OFFLINE GPU RESEARCH SIMULATION
THE ANSWER
PPO > Fixed Rotation
under the locked synthetic evaluation protocol
Verified - pinned model, evidence, provenance, and release gate
Interactive - one shared GPU scenario with locality-level replay
Honest - synthetic scope, historical boundary, and limitations visible
Next: validate with representative operational data and electrical-network constraints
Notes: Close by answering the original question, then transition to the live demonstration. The next scientific step is operational-data and network-constraint validation before any field-facing use.
[Sources]
- docs/RESULTS.md (Result statement; Interpretation)
- docs/REPORT.md
[/Sources]